## Slide 1
Southeastern Georgia VoIP Consortium (SeGA 7)
•Armstrong Atlantic State University, Savannah, GA •East Georgia College, Swainsboro, GA •South Georgia College, Douglas, GA
•Waycross College, Waycross, GA •Liberty Center, Hinesville, GA •Coastal College of Georgia, Camden County, GA
•Coastal College of Georgia, Brunswick, GA
Presented by Scott Gilreath, Manager of Networking and Telecommunications, Armstrong Atlantic State University
Benefits and Challenges of a Multi- University VoIP Consortium Many institutions and early adopters of VoIP technologies have reaped the benefits of cost savings and greater flexibility associated with this communications technology. The challenges and benefits of expanding this technology across a consortium of independent universities, however, are just now being realized Three years into the post- Centrex world, the unique social and technology needs as well as benefits of aligning with other institutions are explored in this session.
Consortium Facts
Implemented December 2007 – First college system in the Southeast to implement this type of collaboration
Contains 5 unique Management teams, support personnel group, and separate networks
Five CBO and CIO input into project
Each Campus can act in LSP (Local Survivable Processor) mode if connectivity to main host is lost
Six unique Local Exchange Carriers (phone companies for long distance and regional calling) are maintained
Toll-Free calling between all campuses is available via SeGA 7 Intranet routes
Technical Facts
Avaya system with over 2000 IP phones combined
Seven distinct local independent network regions involved
Eighteen Local Gateways for direct IP phone connectivity and redundancy
Shared Voice-Mail system –AVST
Protected packet encapsulation with QOS markings between all campus sites
Between 150k and 225k calls per month combined
System functions across multi-vendor local hardware (Cisco, Juniper, HP, etc)

## Slide 2
The Bad
Each local network is independently managed, making for more time-consuming troubleshooting
Quality of Service issues may develop due to lack of complete visibility into all network settings by any one party
IT staff at each institution may not have time to troubleshoot issues locally due to smaller college staffing
Possibility of “too many hands in the cookie jar” effect •Potential for slower decision making process
Lack of local network visibility hinders or prolongs resolution by hosted site Administrator for the Consortium
Service work or required outages must be coordinated based on seven different college schedules
The Good
Loan to be paid off in 2013, with a total time to ROI of only 5 years from start to finish
No point to point calling fees • Consortium able to leverage lower prices for services due to size of combined groups
All support personnel have central contact at Armstrong to work as repair liaison for any issues
Technology partnership allows for greater collaboration with broader scope of IT staff at all colleges
The Not So Ugly
99.98 uptime globally (greater than prior averages with local Centrex providers)
Call Quality on par with Centrex or Pots system •Greater flexibility with call routing, features, and voice-mail options
Required only one additional position to co-manage all seven sites •Enterprise failover solution ensuring uptime
Ability to integrate legacy 1FB phone lines for emergency purposes (elevators, Credit Card machines, Fax lines, etc)
Shared upgrade system cost and shared maintenance fees across entire consortium lowers individual capital expenditures
Monday Morning Quarterbacking
Have all IT parties provide local network architecture before project begins
Require mandatory training before implementation for support staff and local administrative assistants for each department
Investigate integrated Voice-mail solution •Have a slower roll-out schedule •Require E-911 rollout at same time
Obtain 6 month contract with dedicated support technician from vendor until system is well understood